I recently ran into a case where a site was losing about 0.6% of their TCP packets. They were also experiencing broken TCP communication sessions and slow TCP communications when it was working. They never equated the two because they were only dropping about 1 packet in 150 and believed that since TCP retransmits lost packets there shouldn’t be any problems.

To test the effects of lost packets I transferred a 1,822,788-byte file with FTP. The router I used was able to drop packets at a uniform rate. Every 1000th packet for 0.1% loss rate, every 500th packet for 0.2%, every 200th for 0.5%, etc. I transferred the same file 100 times and calculated the minimum, average, and maximum transfer times. Figure 1 shows the results. The transfer took about 3560 packets (512 byte MSS).

As can be seen in figure 1 a 0.5 % (yes I changed from 0.6% to 0.5%) loss rate increased the average transfer time from 7.15 seconds to 20.56 seconds. How can losing 18 packets (0.5% of 3560) have such a large effect? Part of the answer is the delay caused by waiting for the retransmission timer to go off. However, another part of the answer is that TCP assumes that any packet loss is caused by congestion. After a packet loss, TCP slows down its transmission rate to reduce the congestion and then slowly increases it again. If the packet loss is caused by something other than congestion slowing down probably will not help and certainly hurts. How does TCP know that a packet has been lost? Simple, it assumes that a packet has been lost if it needs to retransmit the packet.

The simplest way to determine if packets are being lost is to look at the TCP statistics (see figure 2). For the sender the key statistics are data packets and data packets retransmitted. This gives a count of what percentage of packets needed to be retransmitted and hence where lost. Figure 3 shows these statistics before and after the 0.5% test. The receiving statistics completely duplicate packets, packets with some dup. data and out-of-order packets are not quite as clear-cut. They indicate a lost packet but the statistics may go up several times for just 1 lost packet. For example, if packets 1 thru 5 are sent and 2 is lost then packets 3, 4, and 5 will all increment the out-of-order counter.

Unfortunately, these statistics offer no clues as to why the packets were lost. It could be because the packet itself failed to arrive at the connection’s remote TCP peer or the remote peer’s acknowledgement (ACK) packet failed to arrive back at the module.  To add to our misery, these statistics are for all the TCP connections on the module. If only packets to one network or one remote peer are being lost the ratio of data packets retransmitted to data packets will be significantly smaller than what is really happening on that 1 connection. Note that in figure 3 the calculated drop rate is not quite 0.5%. There wasn’t much other TCP traffic but there was some that was not going thru my special router. What can we do in this case? While not fool proof we can look at the connection’s send queue statistic (see figure 4). This statistic is a count of the bytes of  sent data that have not yet been acknowledged and data waiting to be sent. Under ideal circumstances the number is 0 or very small. If the number grows and shrinks one possibility (and there are several others) is lost packets.

The TCP receive statistics discarded for bad checksums, discarded for bad header offset fields, and discarded because packet too short (back to figure 2) are more clear-cut since they indicate a specific error and a lost packet. However, these errors are very unusual since they require that the sender’s protocol stack have a bug in it or the use of a transport layer that does not do any error checking (SLIP comes to mind) or bad memory in a router or bridge.

Some retransmissions are inevitable but the percentage should be very small. Anything below 0.01% I wouldn’t worry about. For something larger I would ask myself if I’m seeing any problems, if not then I would probably look at the Ethernet statistics (see below) and investigate any problems I see but other wise not worry about it. A lot will depend on the type of traffic on the module. I doubt a telnet user will notice any problems even with a 0.5% retransmission rate but if your users are transferring large amounts of data they should recognize a problem. I would also run ‘netstat –statistics’ to get the statistics at least once a day to create a baseline. This will tell you if packet loss is getting worse over time and if a new problem is related to packet loss. Any significant packet loss should be investigated so you know where the loss is happening. It may be on a segment that you have no control of, i.e. the Internet or on an overloaded device that cannot be upgraded but at least you will understand what is happening and using figure 1 can estimate the effect on your performance.

The “netstat –detail” command (see figure 5) shows statistics about the local Ethernet segment and interface. If there is an increment in the Transmit ring full or Transmit frame discarded, late collisions, or Transmit frame discarded, excessive retry statistics you know that a frame (Ethernet frames transmit TCP/IP packets) has been lost. Comparing the increase in these statistics with the increase in the Transmitted frames statistic will give you the percentage lost.  A late collision is an indication of a network segment that is too long or of a host on the segment that is not listening for collisions. The most common cause of this is a host on the network configured for full duplex while the module is configured for half duplex. A late collision may also be caused by someone plugging in or unplugging an RJ-45 connector from a patch panel, or some device (NIC, hub, or switch). An excessive retry can also be the result a host that is configured for full duplex while the module is configured for half duplex. It can also be the result of a host configured for a smaller than normal inter-frame gap, or a host or hosts creating some kind of traffic storm (the cause at the site I mentioned at the start of this article) or just too many hosts on the segment. If you are getting excessive retry errors you may also be getting Transmit ring full errors since if the card is having problems sending frames while the upper layers are still sending down frames the card’s buffers may become full and drop frames. The cause of any late collisions or excessive retries should be investigated. Note that Transmit frame was deferred, Transmit frame after a single retry, and Transmit frame after multiple retry are not significant and do not indicate any kind of error.

Any of the Receive frame discarded statistics obviously indicate a dropped frame. The bad CRC and improper framing can be the result of a bad cable or connector or the module may be configured for full duplex while its link peer is configured for half. The collision fragments sent by the link peer will be interpreted as these kinds of errors. Some amount of these errors is inevitable but not many. The 802.3 spec calls for a bit error rate on a 10BaseT link of 1 bit per billion bits transmitted. This works out to 1 error for every 82,345 maximum sized frames (1518 bytes) or 0.001%. The bit error rate for 100BaseT is 1000 times smaller.  Anything larger than the spec should be investigated. The lack of buffers, overflow and congestion errors indicate that a frame could not be processed once it was received because there was no buffer space to put it. This typically happens during a broadcast storm, when frames arrive faster then we can process them.

The SQE error is a little tricky to interpret. This will only happen on a K104 and only if the K104’s transceiver does not have SQE (also called, SQE test, SQE heartbeat or heartbeat) enabled. If it’s not enabled then after a frame is transmitted the chip goes through a reset. This takes several 10s of milliseconds, during which no frames can be received. So frames can be lost without any count of them. Unfortunately, it’s also possible that this statistic can go up without any frames being lost so using this statistic to help estimate lost packets is unreliable. However, the K104 requires that SQE be enabled on the transceiver, if this statistic is going up make sure that SQE is enabled and if not, enabled it. If it is enabled try a different transceiver.

So far everything I’ve said has been about OS_TCP, what about STCP? Well the effect of losing TCP packets is the same, that is, throughput drops dramatically. The STCP TCP layer statistics do not provide the same set of statistics as OS_TCP (see figure 6). The counters tcpOutSegs and tcpRetransSegs will tell you what percentage of packets were retransmitted but there is nothing like the receive counters that OS_TCP has. STCP does provide the same Ethernet layer statistics as OS_TCP but uses the command “netstat –interface” instead of “netstat –detail” to display them.

The primary point of this article is contained in figure 1, TCP retransmissions have an effect on the performance of large data transfers that appears to be out of proportion to the actual number of retransmissions. The universe demands that some number of retransmissions are inevitable, however, this should be a very small number. OS_TCP and STCP can give you some clues if the error is caused by a problem on the local Ethernet segment. If not the only thing you can do is slog through each network segment checking for errors and congestion.

Good luck, you’re going need it.

Figure 1 – Minimum, Average, and Maximum transmission times for 100 file transfers with uniform distribution of lost TCP packets.

Figure 2 – TCP statistics to identify when packets are lost

netstat –protocol tcp -display_zeros

tcp:

13523268    packets sent

11231108    data packets (981182197 bytes)

44835    data packets (7843158 bytes) retransmitted

1742770    ack-only packets (1621590 delayed)

0    URG only packets

29719    window probe packets

264677    window update packets

210159    control packets

14714493    packets received

11083836    acks (for 982113504 bytes)

113957    duplicate acks

0    acks for unsent data

5907701    packets (182121329 bytes) received in-sequence

33003    completely duplicate packets (361206 bytes)

22883    packets with some dup. data (39485 bytes duped)

48352    out-of-order packets (8304217 bytes)

7070    packets (11791 bytes) of data after window

7015    window probes

3480    window update packets

67    packets received after close

0    discarded for bad checksums

0    discarded for bad header offset fields

0    discarded because packet too short

162664    connection requests

58172    connection accepts

62439    connections established (including accepts)

222556    connections closed (including 2267 drops)

159460    embryonic connections dropped

10834452    segments updated rtt (of 12960536 attempts)

45506    retransmit timeouts

1214    connections dropped by rexmit timeout

29779    persist timeouts

8481    keepalive timeouts

14    keepalive probes sent

3    connections dropped by keepalive

Figure 3 – data packets before and after the 0.5% test

Before

1460998    data packets (863592337 bytes)

- data packets (1738556 bytes) retransmitted

After

1821964    data packets (1048148001 bytes)

- data packets (2636117 bytes) retransmitted

1821964 – 1460998       = 360966 data packets

5214 -    3459       =   1755 data packets retransmitted

1755 /  360966 * 100 = 0.48% dropped packets

Figure 4 – looking at the send queue to infer (guess about) packet loss

netstat -n; netstat -n; netstat -n

Active Internet connections

Proto Recv-Q Send-Q  Local Address          Foreign Address        (state)

tcp        0     45  198.115.44.11,4806     10.1.1.13,10835        ESTABLISHED

. . .

tcp        0  10956  198.115.44.11,4806     10.1.1.13,10835        ESTABLISHED

. . .

tcp        0   1013  198.115.44.11,4806     10.1.1.13,10835        ESTABLISHED

Figure 5 – Low Level Ethernet Statistics

netstat -detail #e1.22.13

Interface Summary:

Interface Number: 0     Device Name: #e1.22.13       IP Address: phxcac-m1.az.st

+ratus.com

Maximum Transmit Unit (MTU): 1500

Line Speed                 : 10000000

Administrative Status      : UP

Operational Status         : UP

INPUT          OUTPUT

-----          ------

Packets           :     24670252       15813674

Octets            :     1844639441     1746939031

Errors            :     0              0

Discards          :     86396          0

Ucast Packets     :     24636812

NUcast Packets    :     33440

Out Qlen          :     0

Unknown Protocols :     86396

MAC Statistics:

MAC Type   : CSMA/CD                             MAC Address: 00:00:a8:00:a2:0f

Received frames                          : 17009794

Received multicast and broadcast frames  : 7660459

Received octets                          : 2387385252

Transmitted frames                       : 17744975

Transmitted octets                       : 2286231022

LAN Chipset re-initialized               : 5

SQE error                                : 2

Transmit ring full                       : 0

Transmit frame discarded, late collisions: 0

Transmit frame was deferred              : 4615

Transmit frame after a single retry      : 2288

Transmit frame after multiple retry      : 2182

Transmit frame discarded, excessive retry: 138

Receive frame discarded, lack of buffers : 414

Receive frame discarded, improper framing: 0

Receive frame discarded, an overflow     : 0

Receive frame discarded, bad CRC         : 0

Receive frame discarded, bad address     : 0

Receive frame discarded, congestion      : 0

MAC Summary:

Transmitted frames         : 17744975

Transmitted octets         : 2286231022

Retransmitted frames       : 9085

Received frames            : 24670253

Received octets            : 2387385252

Received invalid frames    : 414

Figure 6 – STCP’s TCP layer statistics

netstat -protocol tcp -statistics

tcp:

0  incomplete TCP headers

0  TCP checksum errors

4  tcpRtoAlgorithm

187  tcpRtoMin

281250  tcpRtoMax

5130  tcpMaxConn

1222  tcpActiveOpens

736  tcpPassiveOpens

0  tcpAttemptFails

0  tcpEstabResets

2  tcpCurrEstab

4728565  tcpInSegs

1341948  tcpOutSegs

17421  tcpRetransSegs

0  tcpInErrs

- tcpOutRsts